## Slide 1: UAS Alert

## Slide 2: Team Members
Brian Joyner
Carter Long
Clayton Hudspeth
Brady Wade
Chase Abercrombie
Computer Engineering
Electrical Engineering
Electrical Engineering
Electrical Engineering
Electrical Engineering

## Slide 3: Advisor
Dr. J.W. Bruce
Associate Professor
Mississippi State University
Ph.D., Electrical Engineering, University of Nevada Las Vegas, 2000
M.S., Electrical Engineering, Georgia Institute of Technology, 1993
B.S., Electrical Engineering, The University of Alabama in Huntsville, 1991

## Slide 4: Problem Statement
During a nine month period, November 2014 to August 2015, the FAA reported 764 UAV sightings where the UAV compromised the safety of the aircraft [1].
UAS operators do not have to go through any safety training or certification before being allowed to operate a UAV.
Recent FAA rules allow for a UAV to fly above 400 ft. through a waiver application.

## Slide 5: Solution
Provide UAVs the ability to map and track nearby air traffic.
Create a device that can be easily attached to any UAV.
Give alerts to help mitigate the chance of mid air collisions.

## Slide 6: What is UAS Alert?

## Slide 7: System Overview

## Slide 8: Constraints
Technical
  Transmission
  Device Weight
  Battery Life
  Compact Design
  Response time
Practical
  Safety
  Political
Notes: Here we have our 5 technical and 2 practical constraints.

## Slide 9: Technical Constraints
Transmission
  Line-of-sight range
  Transceiver range > UAV controller range
  900MHz. Not 2.4GHz or 5.8GHz
Device Weight
  Device weight < 300 grams
Notes: First off when communicating with our device we will need a line-of-sight range and need to have a range larger than the UAVs controller range. We used 900MHz so that we do not crowd the commonly used frequencies for UAVs.
Our second constraint is the weight. We need to keep our device weight under the average payload of a UAV which is 300 grams.

## Slide 10: Technical Constraints
Battery Life
  Battery Life > 1 hour (avg. UAV flight time)
Compact Design
  Device does not interfere with flight
  Dimensions - 150x150x100 mm (LxWxH)
Response Time
  Response time < 1 minute
Notes: Since our device must protect airplanes throughout the duration of the UAVs flight time we need our battery to power our device for more than an hour which is the average flight time of a UAV.
Our design must also not interfere with the UAVs standard operations. To do this our device needs to have the dimensions here which is the available space on average size UAVs.
Our response time must also be fast enough to give accurate alerts and notifications for the operator.

## Slide 11: Practical Constraints
Safety
  Real time mapping
  Accurate Results
  Alerts to keep pilots safe
Political
  Can only use ADS-B IN
  Cannot broadcast on unauthorized frequencies
Notes: Now for our Practical constraints. Safety is a key component of our project. We are using real time air traffic mapping to keep pilots safe.
Political is our other main constraint because we are not legally able to broadcast on certain frequencies. Therefore we are just using ADS-B IN to listen certified broadcasting.

## Slide 12: Approach

## Slide 13: Hardware
Batteries
Antennas
Transceivers
Software-defined Radios
Notes: The Hardware we are using is Batteries, Antennas, Tranceivers, and Software-defined Radios.

## Slide 14: Power
 | Current Draw | Voltage | Power Draw
SDR (x2) | 290 mA-hr each | 5 V | 2.9 W-hr
Raspberry Pi | 400 mA-hr | 5 V | 2 W-hr
Transceiver | 215 mA-hr | 2.1-3.6 V | 0.46-.774 W-hr
Needed | 1.195 A-hr | 5 V | 5.975 W-hr
Notes: Here we have the table that breaks down the power usage of our on board device. We will be powering 2 SDRs, a Raspberry Pi, and a Transceiver. The overall Current usage and power draw are shown in te Needed row.

## Slide 15: Battery Comparison
Tenergy | Turnigy
3.7 V 500 mAh 57x18.5x7.8 mm 17 Grams | 7.4 V 1200 mAh 116x17x13 mm 55 Grams
✔
Notes: These are the 2 batteries we have looked at, the Tenergy and the Turnigy. We decided on the Turnigy battery because it met our voltage and Amperage requirements to meet our flight time constraints.

## Slide 16: Antennas
Designs Considered:
Monopole
Dipole
Folded Dipole

## Slide 17: Antennas
Dipole
Much higher dBi over folded dipole design increasing range.
Does not require a ground plane that allows for interference from circuit board signal paths due to compact design.
Advantages for Application Constraints:

## Slide 18: Antennas
Designs Considered:
Monopole
Dipole
Folded Dipole
✔

## Slide 19: Transceivers
Synapse RF266PC1 |  |  | XBee 900HP |  | 
 | Operating Frequency Band | ISM 2.4GHz |  | Operating Frequency Band | ISM 902 to 928MHz
 | Encryption | AES 128-bit |  | Encryption | AES 128-bit
 | Line-Of-Sight Range | Up to 4,000 feet at 250Kbps |  | Line-Of-Sight Range | Up to 1,000 feet at 200Kbps; Up to 4 miles at 200Kbps (w/2.1dBi dipole)
 | Antenna Options | Chip Antenna |  | Antenna Options | Wire; Optional 2.1dBi dipole
 | Receiver Sensitivity | -103dBm |  | Receiver Sensitivity | -101dBm

## Slide 20: Transceivers
XBee 900HP
Operates on the 902 MHz to 928MHz scale which reduces signal interference from smaller objects within LOS range.
Longer range when standard wire antenna is replaced with 2dbi high gain antenna.
Advantages for Application Constraints:

## Slide 21: Transceivers
Synapse RF266PC1 |  |  | XBee 900HP |  | 
 | Operating Frequency Band | ISM 2.4GHz |  | Operating Frequency Band | ISM 902 to 928MHz
 | Encryption | AES 128-bit |  | Encryption | AES 128-bit
 | Line-Of-Sight Range | Up to 4,000 feet at 250Kbps |  | Line-Of-Sight Range | Up to 1,000 feet at 200Kbps; Up to 4 miles at 200Kbps (w/2.1dBi dipole)
 | Antenna Options | Chip Antenna |  | Antenna Options | Wire; Optional 2.1dBi dipole
 | Receiver Sensitivity | -103dBm |  | Receiver Sensitivity | -101dBm
✔

## Slide 22: Software-Defined Radios (SDR)
Software-defined radios are radios where typical radio components such as demodulators are implemented in software
RTL-SDR is Digital Video Broadcasting USB dongle used as an SDR
The RTL2832U is a high-performance DVB-T demodulator IC that supports a USB 2.0 interface [2].
Uses Rafael Micro R820T2 tuner IC tunes to desired frequency

## Slide 23: Software-Defined Radios
SDR | Frequency Range | Frequency Stability | Weight | Price | Choice
NooElec NESDR Nano 2+ | 25-1750 MHz | 0.5PPM | 17 grams | $22.95 | ✓
NooElec NESDR SMArt | 25-1750 MHz | 0.5PPM | 28 grams | $21.95 | 
RTL-SDR.com | 0.5-1700 MHz | 1PPM | 31 grams | $24.95 | 

## Slide 24: Software-Defined Radios
SDR | Frequency Range | Frequency Stability | Weight | Price | Choice
NooElec NESDR Nano 2+ | 25-1750 MHz | 0.5PPM | 17 grams | $22.95 | ✓
NooElec NESDR SMArt | 25-1750 MHz | 0.5PPM | 28 grams | $21.95 | 
RTL-SDR.com | 0.5-1700 MHz | 1PPM | 31 grams | $24.95 | 

## Slide 25: Software-defined Radios
NooElec NESDR Nano2+
NooElec NESDR SMArt
RTL-SDR.com SDR

## Slide 26: Software
Linux-based Operating System
Ground Station
Demodulation Software
Display and Alerts
Code will be written in Python and C/C++

## Slide 27: Operating System
Demodulation software used is designed to run on a linux-based system
PiAware runs on linux-based machines (Ubuntu, Raspbian)

## Slide 28: Ground Station
Makes use of services from FlightAware
Multilateration (MLAT)
Interpretation of messages
Decides whether or not to upload to FlightAware

## Slide 29: Demodulation Software
Dump1090/Dump978
Software on-board will simply demodulate, parse (remove unneeded data), and repeat to ground station
Decodes a variety of message formats including DF17 (ADS-B)
Features 24-bit Cyclic Redundancy Check (CRC) for error correction (Very important to have correct data)

## Slide 30: Display and Alerts (User Interface)

## Slide 31: Design Plan
Test everything through Transmission Control Protocol (TCP) sockets
Use simulation software to test possible flight conditions before implementation
Simulation data will feed to “on-board module” which will feed to the ground station.
Modular testing
Weekly goals

## Slide 32: Testing Diagram

## Slide 33: Timeline
 | August | September | October | November | December
Research |  |  |  |  | 
Prototyping and Software |  |  |  |  | 
Testing and Debugging |  |  |  |  | 
Final Design Changes |  |  |  |  | 

## Slide 34: Progress
Ordered parts
Able to receive signals on 1090 and 978, and send raw data packets through a TCP connection simulating the air-to-ground datalink. (From RPi to Laptop)
Mostly researching, it’s a broad field.

## Slide 35: References
[1]"A320 collision heightens UAV safety concerns", Flightglobal.com, 2016. [Online]. Available: https://www.flightglobal.com/news/articles/a320-collision-heightens-uav-safety-concerns-424419/. [Accessed: 30- Aug- 2016].
[2]"Realtek", Realtek.com.tw, 2016. [Online]. Available: http://www.realtek.com.tw/products/productsView.aspx?Langid=1&PFid=35&Level=4&Conn=3&ProdID=257. [Accessed: 06- Oct- 2016].

## Slide 36: Questions?